## Slide 1: 1.As the engineer officer of the watch list eight reasons for calling the Chief Engineer Officer (8)
Fire
Major engine failure/breakdown
Blackout
Medical emergency
Prior to departure
Before arrival into port/standby
Flooding of machinery spaces
Relieving engineer is drunk
And many more….

## Slide 2: 2. Describe eight actions to be taken by the relieving Engineer Officer of the Watch before taking charge of the watch (8)
Inform EOOW you are entering machinery space
The main thing here is pre watch rounds which must include;
  Check funnel for smoke
  Check economisers
  Check header tanks
  Check main engine cylinder heads
  Check turbocharger
  Check crankcase relief doors for evidence of lift
  Check OMD
  Check boiler
  Check condition of bilges
  Check around general machinery….
Enter ECR and check machinery space log book
Check the switchboard
Check for any active permits
Check ORB
Handover with EOOW
Are they any standing orders from the CE?
Are we expecting heavy weather?
Are we going on standby within my watch?
Ask lots of questions, the watch is going to be your responsibility!

## Slide 3: 3. State four engine room records that are kept and state why they are important (6)
Oil Record Book
  In order to comply with MARPOL legislation
  If not properly maintained your ship may lose their IOPPC (International Oil Pollution Prevention Certificate) and could be detained or heavily fined by port state and flag state control
  The EOOW could also be personally fined or even imprisoned
Machinery space log book
  This gives the EOOW a really detailed picture of what is going on
  Collating all machinery readings into one log can highlight machinery that is not operating efficiently and requires action
Permit to work
  This allows the EOOW to see exactly what work is going on around the vessel
  For example an activation of a fire detector in the machinery space will be treated differently if the EOOW knows there is a hot work permit active for welding in that compartment
Engine Room Signing In Book
  This is a very important record. It means the EOOW knows if there are any non-technical personnel within the machinery space and can act accordingly in the event of an emergency
  In the unlikely event of CO2 being released into the space all persons must exit the machinery space, therefore we must know exactly who is in the machinery space AT ALL TIMES

## Slide 4: 4. State the checks to be made on the steering gear prior to leaving port.
Check for oil leaks and any loose linkages on the steering gear.
Check steering gear flat bilges for signs of oil or water
Check for correct oil level and test low level alarm.
Run one unit at a time, 30 degrees to 35 degs.in 28 sees at full power.
Where only one main unit is fitted with an aux. unit. the auxiliary unit must go from 20 degrees. to 20 degrees. In 60 secs. at 8 knots or half speed.
Test the communication link between the Bridge and the Steering compartment.

## Slide 5: 5. Give the correct procedure for starting an air compressor
Check the oil level
Check the cooling water.
Ensure that the inter stage drains are open.
Check that all the correct valves are open fully to the air receiver and that there is sufficient capacity available in the air receiver...
If a manual unloader is fitted ensure that it is open. (machine must be started in the unloaded position).
When the machine is up to speed, close the unloader and the interstage drains.

## Slide 6: 6. Describe how to prepare main engine from cold to ready to Standby, including any tests that requires being carried out.
Before a large diesel engine is started it must be warmed through by circulating hot water through the jackets etc. This will enable the various engine plans to expand in relation to one another and allow the engine load to be increased sooner rather than later.
The lubricating oil should as be heated and circulated around the bearings etc., and the piston if oil cooled.
The various return pipes on both the water and oil systems should be checked to ensure no blockages and the return temperatures should be monitored.
The various supply tanks, filters, valves and drains are all to be checked and opened or closed as required.
All control equipment, alarms etc. should be examined for correct operation.

## Slide 7: 6. Describe how to prepare main engine from cold to ready to Standby, including any tests that requires being carried out.
The indicator cocks should be open and the turning gear engaged and started to ensure that there is no water present in the cylinders. If any water issues further investigation can be carried out to ascertain the cause.
All oil levels should be checked, i.e. Sump, turbochargers, governors etc.
The fuel oil system can be lined up and circulated with hot fuel.
Any scavenge blowers if manually operated, should be started.
Manually operate the cylinder lubricators.
The turning gear should be removed and the engine blown over on air before closing the indicator cocks.
The engine is now available for standby.