## Slide 1: Deck Cargo
It is loaded, now, how to secure it?

## Slide 2: Deck Cargo
What can we use?
Wires, Chains, Rope, “Tomming-off”, Brackets, Welding, Straps, Blutack, Double-sided Sellotape, Gravity, Prayer, ?

## Slide 3: Deck Cargo
Wires
Chains All these require some form of
Rope Tightening Device.
Straps
“Tomming-off”
Brackets
Welding
Blutack, Gravity, Gaffer Tape,
Double-sided Sellotape, Prayer,
Can we take these as “non-starters”?

## Slide 4: Deck Cargo
Wires & Turnbuckles.
All lashings have to be independent, all items within the lashing system have have to be strength tested, so there are no weak parts.
A rough guide: a 32mm wire lashing system with all the correct size turnbuckles, shackles &etc will have a SWL of around 20mt.

## Slide 5: Deck Cargo
Chain with tensioner.
Such an arrangement (top right) would be able to be hand-carried, links of around 100mm & have a SWL of around 10mt.

## Slide 6: Deck Cargo
Ratchet Straps.
A combined system that has its own tightening and locking device, strength varies with size & construction.
A 50mm ratchet strap would have a SWL of around 5mt.

## Slide 7: Deck Cargo
Ropes.
A very flexible system, however, not very strong.
A 24mm polyprop rope lashing would have a SML of around 4mt.

## Slide 8: Deck Cargo
“Tomming Off”
The art of putting timber baulks between the cargo & a solid surface to stop the cargo moving.
Red bit is timber, yellow bit is wire/chain, black bit is ship structure, eg deck & hatchcoaming.
As strong as your timber!

## Slide 9: Deck Cargo
Brackets.
An idea that you place the cargo on deck & weld brackets around it to hold it in place, brackets should be welded close-up to the item. Brackets should be steel & 150-200mm high, 300ishmm in length. It works.

## Slide 10: Deck Cargo
Weld.
Simply weld the cargo to the deck or hatch-cover!
Approximate strengths are around 1mt per cm of decent welding.
Don’t try welding trucks or wooden boxes to the deck, it isn’t always successful.

## Slide 11: Deck Cargo
So how many lashings should I use?
At this level (calculations come in HND) a good “rule of thumb” would be to use 3 times the weight of the cargo.
So for a 100mt piece of cargo, 300mts-worth of SWL is required: so if using a 32mm wire system with SWL = 20mt, you require 300 / 20 = 15 lashings.
These should be 100mt-worth on each side, with the other 100mt-worth split between Ford & Aft.

## Slide 12: Deck Cargo
Bits to remember:
Lashings should be independent.
Lashings should lead down at between 30 & 50 degrees to be effective.
Lashings should be all at the same tension, one tighter than the rest will take all the strain & BREAK
Lashings are to be inspected, adjusted & logged daily.